## Slide 1: We found Wireless in a wired place
Rushad Antia

## Slide 2: Contents
Motivation / Objectives
Software
Testing Setup
Tests
Conclusion

## Slide 3: Disclaimer
"Certain commercial equipment, instruments, or materials are identified in this paper in order to specify the experimental procedure adequately. Such identification is not intended to imply recommendation or endorsement by the National Institute of Standards and Technology, nor is it intended to imply that the materials or equipment identified are necessarily the best available for the purpose."

## Slide 4: Motivation
Can wireless replace wired in a factory setting?
Wired | Wireless
+ Reliable | + Inexpensive
+ More secure | - Prone to attacks
- Expensive | - Unreliable

## Slide 5: Objectives
Develop a Publish/Subscribe network package in Node.js (javascript)
Create a tool to monitor sensor nodes
Create tools to log and capture data from nodes
Connect nodes to RF Channel Emulator to test performance of wireless in simulated environments
Analyze Data

## Slide 6: Software

## Slide 7: Publish / Subscribe Network
Written in Node.js
Each node acts as a client and server
Nodes connect to a “Master Node” that brokers connections between nodes
Nodes connect over TCP/IP to other nodes and subscribe to topics that other nodes publish
Edison03
Has: Button
Wants: Light
Edison01
Has:
Wants: Button, Light
Edison05
Has:
Wants: Button, Light

## Slide 8: Node Joining the Network
Edison03
Has: Button
Wants: Light
Edison01
Has:
Wants: Button, Light
Edison04
Has:
Wants: Button, Light
Edison05
Has:
Wants: Button, Light
Edison06
Has:
Wants: Button, Light
Edison03
Has: Button
Wants: Light
Edison01
Has:
Wants: Button, Light
Edison04
Has:
Wants: Button, Light
Edison05
Has:
Wants: Button, Light
Edison06
Has:
Wants: Button, Light
Edison02
Has: Light
Wants: Button

## Slide 9: Master Node
Server that runs on a PC on the network
Brokers the connections between nodes based on their Publish/Subscribe needs
Acts as a webserver that hosts a website to monitor and interact with all alive nodes on network
Each node connects to this node through TCP/IP

## Slide 10: Edison Control Center

## Slide 11: Testing setup

## Slide 12: Testing Setup
“Edison03” node emits a ON/OFF pulse (button push) to all nodes in the network every 100ms
Events emitted over TCP/IP through the router in infrastructure mode
Nodes connected to RF Channel emulator to simulate various environments

## Slide 13
Signal Generator
Oscilloscope
Edison03
Edison01
Edison02
Edison05
Edison06
RF Channel Emulator
Wi-Fi Router
PC

## Slide 15: Testing

## Slide 16: Test Cases
The RF Channel Emulator allows us to create a multitude of test cases
180 tests total
802.11 b/g
802.11 n
Mobile
Stationary
Free space
Line of sight
No line of sight
20 MHz
40 MHZ

## Slide 17: Example Data capture
Captured oscilloscope data through PC and exported to csv
Imported csv capture into MATLAB to compute latency between devices